## Slide 1
Number Plate Detection System using ESP32-CAM
Group no 24
Group Numbers:
  M.RAHULAN 2022T01342
  B.NILUKSHAN 2022T01329
  MS SAFNI 2022T01351
  MJM ARSATH 2022T01266
Department of Instrumentation and Automation Technology
Faculty of Technology, University of Colombo
IA 1209-Design Project
(Batch 2021/22)

## Slide 2
Project Overview
Develop a real-time number plate detection system using an ESP32-CAM for image capture and a laptop server for processing, recognition and data store.
ESP32-CAM
Image capture and display control.
Laptop Server
OpenCV + EasyOCR for recognition.
OLED Display
Displays recognized numbers.
Push Button
triggers capture.
Wi-Fi
Enables device communication.

## Slide 3
System work Flow
Capture Image
Press reset to trigger ESP32-CAM image capture.
Send to Server
ESP32-CAM sends image to laptop via HTTP POST.
Process & Recognize
Laptop uses OpenCV and EasyOCR for recognition.
Save Data
Detected number saved to file (e.g., numbers.txt).
Return & Display
Server sends number back to ESP32-CAM for OLED display.

## Slide 4
Hardware and Software Components
Hardware
  ESP32-CAM Module: Integrated camera for image capture, Wi-Fi for data transfer.
  OLED Display (SSD1306): Compact screen for displaying detected numbers.
  Push Button: Triggers image capture and system reset.
  Laptop: Acts as a server running Python with Flask, OpenCV, and EasyOCR.
Software
  ESP32-CAM Code: Utilizes WiFi.h, HTTPClient.h, Adafruit_SSD1306.h, and esp_camera.h for image capture, server communication, and OLED display.
  Laptop Server Code (Flask): Employs Flask for web requests, OpenCV for image handling, and EasyOCR for number plate OCR.

## Slide 5
System Design Diagram
FTDI Breakout Module: Used to interface the ESP32-CAM with a computer for programming or communication
Trigger Button: Used to trigger certain actions, such as taking a photo or initiating a process.
.
.

## Slide 7: Working video

## Slide 8
Esp32 cam code:
ESP32-CAM Configuration
The ESP32-CAM is configured with Wi-Fi credentials and camera settings for optimal image capture. Key aspects include pin assignments and image quality parameters to ensure clear number plate readings.
Key Functions
  setupCamera(): Initializes camera hardware and pin configurations.
  captureImage(): Acquires image frame buffer and handles HTTP POST requests to send the image data to the server.
  Ftdi module use to program the esp32 cam
  We use c++ programming language in the aurdino ide to program the esp32 cam
  5 Libaries in code structrue
#include <WiFi.h>
#include <HTTPClient.h>
#include <Adafruit_GFX.h>
#include <Adafruit_SSD1306.h>
#include "esp_camera.h“
// Replace with your network credentials
// OLED settings // Push button pin // Camera Pins for AI Thinker ESP32-CAM //main function (void startCamera())

## Slide 9
Server Code (Flask) and EasyOCR Integration
Flask Server
The Flask server acts as the central processing unit, receiving image data via HTTP POST requests from the ESP32-CAM. It leverages Python libraries to perform the core recognition tasks.
EasyOCR for Recognition
  Text Detection: EasyOCR efficiently detects and extracts text from images, crucial for diverse number plate formats.
  Multi-language Support: Extensible for global application, supporting various character sets.
  Real-Time Feedback: Recognized numbers are swiftly returned to the ESP32-CAM for immediate display, enhancing user experience.
from flask import Flask, request, jsonify
import easyocrimport cv2
import numpy as np
app = Flask(_name_)reader = easyocr.Reader(['en'])
@app.route('/upload', methods=['POST'])def upload_image():
img_bytes = request.data
nparr = np.frombuffer(img_bytes, np.uint8) img = cv2.imdecode(nparr, cv2.IMREAD_COLOR)
# Run OCR results = reader.readtext(img)
if results: number_plate = results[0][1] print("Detected:", number_plate)
# Save to file with open("numbers.txt", "a") as f: f.write(number_plate + "\n")
return number_plate
else: return "No Plate Detected", 400
if _name_ == '_main_':
app.run(host='0.0.0.0', port=5000)

## Slide 10
Key Applications
Real-Time Monitoring
Vehicle tracking in parking lots, toll gates, and security systems.
License Plate Recognition (LPR)
Automated systems for law enforcement, access control, and traffic.
IoT Integration
Seamlessly integrates with smart cities and other IoT applications.

## Slide 11
Future Improvements and Applications
Enhancements
  Accuracy: Fine-tune the OCR model for diverse plate formats.
  Machine Learning: Integrate advanced models for robust recognition.
  Range: Upgrade camera resolution for superior image quality.
  Edge Computing: On-device processing to reduce server dependency.
Applications
  Real-Time Monitoring: Parking lots, toll gates, security.
  LPR Systems: Law enforcement, access control, traffic.
  IoT Integration: Smart cities and vehicle monitoring.

## Slide 12
System Functionality & Testing
1
Image Capture
ESP32-CAM successfully captures and sends images to the server.
2
Number Plate Recognition
Laptop server processes images and recognizes number plates.
3
OLED Display
ESP32-CAM displays the recognized number correctly on the OLED.

## Slide 14
Conclusion
Developed a number plate detection system using ESP32-CAM and a Python server. It captures, processes, and displays results. Challenges included Wi-Fi stability and OCR optimization. Future work involves large-scale implementation in parking management or law enforcement.

## Slide 15
Thank You!
Questions and Discussions